## Slide 2
Overview of oneM2M: The National Standard for IoT
Aurindam Bhattacharya
C-DOT
IoT Standards and Smart Cities : India Perspective

## Slide 3: M2M/IoT: Surge of connected things
1 Source: Statista
Connected Home
Transforming industries with innovative services and useful information
Interconnected devices forecast
8.74 Billion (in 2020)
to
25.4 Billion(in 2030)
Automotive
Smart Cities
Retail
Education
Healthcare
Industrial
3

## Slide 4: IoT and M2M framework
Communications network
Field area network
Applications
A
Device
A
Device
A
Device
GW
A
Device
Things
Things
representations
Blood pressure
Pulse oximeter
Pedometer
Smart bandage
Smart phone serving as an M2M device
Communications network
Applications
Linked things and digital
representations

## Slide 5
Present IoT/M2M Deployment Architecture
A
Pipe (vertical):
1 Application, 1 NW, 1 (or few) type of Device
Local N/W
Business Application
Device
Communication Network (mobile, fixed, Powerline ..)
Gateway
Business platform
A
Application Entity

## Slide 6
Pipe (vertical):
For Transport
Local N/W
Transport Application
Device
Communication Network (mobile, fixed, Powerline ..)
Gateway
Transport platform
A
Pipe (vertical):
For Health
Local N/W
Health Application
Device
Communication Network (mobile, fixed, Powerline ..)
Gateway
Health platform
A
Pipe (vertical):
For Health
Local N/W
Metering Application
Device
Communication Network (mobile, fixed, Powerline ..)
Gateway
Metering platform
A
Each Domain/Vertical : A separate Silo
Other domains/ verticals
Present IoT/M2M Deployment Architecture

## Slide 7: OneM2M Architecture Approach

## Slide 8
Today each vertical develops the whole technology stack, leading to silos and cross vertical interoperability issues
Connected Home
Automotive / Connected Car
Smart Cities
Utilities
Supply Chain / Industrial IoT
Healthcare / Fittnes
Connectivity
IoT Service Enablement Functions
IoT Applications
Data storage
Data Analytics
Data presentation
A global interoperable Standard, enables a cross-vertical IoT Eco-System

## Slide 9: oneM2M Breaks Down the Silos
9
Smart
Health
Smart
Transportation
Smart
Metering
Vertical
Information Flow
Vertical
Information Flow
Vertical
Information Flow
Horizontal
Information Flow
Smart
Transportation
Service Layer
…
…
…
Smart
Health
Smart
Metering

## Slide 10: Present Landscape of IoT Applications In Smart Cities

## Slide 11: Deployment Scenarios: Multi User, Shared

## Slide 12
Deployment Scenarios: Brownfield + Greenfield

## Slide 13
  Applications access the Connectivity Layer and built-in sensors, via API’s provided by the Operating System
  Operating System collects connectivity requests from applications, buffers messages, optimizes & controls device’s network use
  Connectivity Layer provides device access to the Internet via the 3GPP mobile network, Wi-Fi, etc..
A framework for developers!
Similar to the modularity of smart Phones -
Operating System
Applications
Governance:
Connectivity
Apply the concept of an Operating System to IoT Devices and Application Developers

## Slide 14: Scope of and purpose of IoT technology Layers
Connectivity Layer
Service Layer
IoT Application
Measuring of Physical Parameters
Execution of commands
Storing of data in case of lack of connectivity
Security, Authentication & Authorization
Device Management & Firmware update mechanism
Connectivity Management
Developer API
IoT Field Device(s)
IoT Infrastructure
UI / Presentation of Device Data
Data Analytics etc.
Developer API to control:
  Data Management
  Security
  Device Management
  Connectivity Management
Reliable & efficient data transport
Reliable & efficient data transport

## Slide 15: Individual technologies / Protocols used today
Connectivity Layer Standards
Service Layer Standards
IoT Application
IoT Field Device(s)
IoT Infrastructure

## Slide 16: Bundling of individual service Layer technologies by oneM2M
Connectivity Layer Standard
Service Layer Standards
IoT Application
IoT Field Device(s)
IoT Infrastructure

## Slide 17: Functions provided by oneM2M
IoT Field Device(s)
IoT Infrastructure
oneM2M Common Service Layer
IoT Application
Application developers can leverage
Common Service Functions (CSF’s) provided by oneM2M
Registration
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure
Semantics
Transaction Management
Service Layer
Time Management
New Addition in oneM2M Release 4

## Slide 18: The Common Service Functions in oneM2M Architecture
Registration
Security
Discovery
Group Management
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management and Delivery Handling
Service Charging & Accounting
Location
Network Service Exposure
CSE
HTTP(S)
CoAP
MQTT
WebSocket
Devices/ Sensors
Applications in the Cloud
Transaction Management
Semantics
Time Management

## Slide 19: Details of the Common Service Functions (CSFs)
Registration
Security
Discovery
Group Management
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management and Delivery Handling
Service Charging & Accounting
Location
Network Service Exposure
Registers the Applications with the CSE
Discovery of the resources within the CSE
Ensures security of the data as well as communication
Grouping the devices/sensors and taking common action
Managing Storage of Data within CSE
Notifying Applications about Data arrival or Events
Management of Devices
Management of Applications and Service Subscriptions
Location data management
Choosing optimal network for application & Device Triggering,
When and How often communication should happen
Providing Charging Data (Records for Billing)
Transaction Management
Semantics
Scheduling of a transaction, locking and unlocking of resources targeted by a transaction
Enable applications to manage semantic information and provide functionalities based on this information

## Slide 20: Industry collaboration around oneM2M

## Slide 21
Connectivity Layer Standards
Service Layer Standards
IoT Application
oneM2M Application Developers Interface
oneM2M Common Service Layer
IP Communication
Connectivity Layer
IoT Field Device(s)
IoT Infrastructure
Developer-Interface

## Slide 22: Topology
Application Service Node
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
AE: Application Entity
CSE: Common Services Entity

## Slide 23: RESTful Style & Access Control
Application Service Node
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
Door Lock
Resources = State Information

## Slide 24: IoT Application Deployment in a multi Service Provider scenario
MN-Middle Node :oneM2M Gateway Device (Contains CSE and optionally applications)
ADN-Application Dedicated Node :The oneM2M Device that contains applications which interface with sensors/actuators
ADN
Smart Parking
Smart Street Light
Smart Metering
Intelligent Transport
IN-CSE (M2MSP-1)
IN-CSE (M2MSP-2)
MN
MN
MN
MN
ADN
ADN
ADN
24

## Slide 25
Functional Roles in the M2M/IoT Ecosystem
USERS
IoT/M2M Application Provider
IoT/M2M platform/Service Provider
IoT/M2M Applications
COMMON SERVICE LAYER
UNDERLYING NETWORK
Underlying Network Service Provider
  Functional Role Description
The User (individual or company) fulfils all of the following criteria:
    Uses an M2M solution.
The Application Service Provider fulfils all of the following criteria:
    Provides an M2M Application Service.
    Operates M2M Applications.
The M2M Service Provider fulfils all of the following criteria:
    Provides M2M Services to Application Service Providers.
    Operates M2M Common Services.
The Network Service Provider fulfils all of the following criteria:
    Provides Connectivity and related services for M2M Service Providers.
    Operates an Underlying Network. Such an Underlying Network could e.g. be a telecom network.
Any of the above functional roles may coincide with any of the other roles.
These functional roles do not imply business roles or architectural assumptions.

## Slide 26: IoT System Deployment View

## Slide 27: The Smart City ICT Reference Architecture for India
Sensor Layer
(IoT)
Network Layer
(IoT)
Common Service Layer
(IoT)
Application Layer
(IoT)
oneM2M Layered architecture
Non IoT Data
City Infrastructure
(Fibre, Sewage, Waste Mgmt., Electricity ….)
Sensing & Actuation(IoT)
Standards compliant IoT Platform
(Common Service Functions)
Data Layer
Network Layer(LMCP and WAN)
(WiFi, 2G/3G/4G/5G, 802.15.x,LoRa, Sigfox, FTTx etc.)
Governance, Operations, Security
Smart City ICT architecture
Data Exchange
(IUDX)
Data Semantics and Ontologies
Urban Services
(API Mgmt, Service Catalog,
Urban Context
(Geo Spatial Registries, Asset Registries etc.)
IUDX Connector/ Adaptors
Public/
Developer
Application Layer
Smart Governance (CCSG)
IUO
ICCC
Citizen App
Smart Lighting, Smart Parking, Smart Home…..
(NGSI-LD +)
Non IoT
Proprietary IoT Platform
IPE
(Adapter)

## Slide 28
Thank You
Aurindam Bhattacharya
aurindam@cdot.in
Notes: 28